## Slide 1: O.C.G.A. Title 12 Chapter 7
The Georgia erosion & Sedimentation Act of 1975
Level 1B: Advanced Fundamentals
Effective August 2018
Notes: O.C.G.A. – Official Code of Georgia Annotated
Title 12 – Conservation & Natural Resources
Chapter 7 – Control of Soil Erosion & Sedimentation

## Slide 2: Overview
Key Definitions – Slide 7
LIA Requirements – Slide 13
Permitting Process – Slide 19
Enforcement – Slide 25
Exemptions – Slide 33
Education & Training – Slide 46

## Slide 3: Key Points
Erosion in Georgia is the result of several activities including construction, agriculture, forestry, etc.… that convert land from one use to another
Land disturbing activities are governed on the federal, state, and local level
GESA is the State Law that may be incorporated into a local ordinance and enforced by a county or municipality
Sometimes referred to as the “E&S Act”

## Slide 4: History of GESA
On April 24th, 1975, the Honorable George Busbee, Governor of the State of Georgia, signed into law as Act 599, the Erosion & Sedimentation Act of 1975 (O.C.G.A. 12-7-1 et. seq.)
With the passage of the E&S Act, Georgia joined very few states that had adopted legislation specifically designed to protect soil and water resources

## Slide 5: Intent of GESA
To strengthen and extend the present erosion and sediment control activities and programs of this state
To provide for the establishment and implementation of a state-wide comprehensive soil erosion and sediment control program
To conserve and protect the land, water, air, and other resources of the state
O.C.G.A 12-7-2

## Slide 6: Participating Agencies
Local Issuing Authorities (LIA)
Soil & Water Conservation Districts (SWCD)
Georgia Soil & Water Conservation Commission (GSWCC)
Georgia Environment Protection Division (GA EPD)
Natural Resources Conservation Service (NRCS)
Contact information for each agency can be found in the
“Resource Information” section

## Slide 7: Key Definitions
O.C.G.A. 12-7-3
*A complete listing of all Definitions can be found in the
“Resource Information” section

## Slide 8: “Plan”
An “Erosion & Sediment Control Plan” is a plan for the control of soil erosion and sediment resulting from a land-disturbing activity
O.C.G.A. 12-7-3(8)

## Slide 9: “Land-Disturbing Activity”
Any activity which may result in soil erosion from water or wind and the movement of sediments into state water or onto lands within the state, including, but not limited to:
    Clearing
    Dredging
    Grading
    Excavating
    Transporting
    Filling of land
O.C.G.A. 12-7-3(9)

## Slide 10: “Local Issuing Authority”
The governing authority of any county or municipality which is certified pursuant to subsection (a) of Code Section 12-7-8 (Certified by GA EPD)
Please refer to the “Resource Information” in the back of this section for a complete listing of all Local Issuing Authorities in the State of Georgia
O.C.G.A. 12-7-3(10)

## Slide 11: “Manual”
The “Manual for Erosion & Sediment Control in Georgia” is the published guidance of the GSWCC governing the design and practices to be utilized in the protection of this state’s natural resources from erosion and sedimentation which shall be based upon sound engineering principles and repeatable bench and field testing of structural and vegetative best management practices
O.C.G.A. 12-7-3(10.2)

## Slide 12: Overview Council
Purpose
  Approve the Manual for Erosion & Sediment Control in Georgia prior to publication by GSWCC
  Provide guidance on the installation and maintenance of best management practices for the preparation of plans
Composed of 9 members
  House of Representatives
  Senate
  GA DOT
  GA EPD
  State & Road Tollway Authority
  Environmental Engineer
  Highway Contracting Industry
  Electric Utility Industry
  Chairperson
O.C.G.A. 12-7-7.1(f)(1-2)

## Slide 13: LIA Requirements & Responsibilities
O.C.G.A. 12-7-4
O.C.G.A. 12-7-7
O.C.G.A. 12-7-8

## Slide 14: Local Ordinance
The EPD may certify a county or municipality as a Local Issuing Authority if the county or municipality enacts an ordinance which meets or exceeds the standards, requirements, and provisions of GESA and the State General Permit
Any land-disturbing activities by a Local Issuing Authority shall be subject to the same requirements of the ordinances such Local Issuing Authority adopted pursuant to this chapter as are applied to private persons, and the division shall enforce such requirements upon the Local Issuing Authority
O.C.G.A. 12-7-8(a)(3)

## Slide 15: Local Ordinance
Cannot be more stringent for:
  Monitoring
  Reporting
  Inspections
  Design standards
  Turbidity standards
  Education & Training requirements
May be more stringent for:
  Additional Buffers
  Project size*
  Other related ordinances such as:
    Tree protection
    Flood plain protection
    Stormwater management
*Project size thresholds with regard to education and training requirements cannot exceed the state general permit
O.C.G.A. 12-7-4(a)
O.C.G.A. 12-7-8(a)(1)

## Slide 16: Responsibilities of Certified LIA
Process applications
Forward ES&PC plans to SWCD for review
Issue permits
Maintain list of active permits
Conduct inspections
Enforce ordinance
Collect fees
Handle complaints
O.C.G.A. 12-7-7

## Slide 17: Memorandum of Agreement (MOA)
When a certified LIA demonstrates the capability to review and approve ES&PC plans AND requests an agreement with the SWCD to conduct such review and approval,
The LIA enters into an agreement with the SWCD & GSWCC to conduct plan review “in-house”
  Can result in a quicker turn around time
Please refer to the “Resource Information” for a complete listing of all LIA’s with a Memorandum of Agreement
O.C.G.A. 12-7-7(2)(e)
Notes: Responsibilities of a LIA with MOA are the exact same

## Slide 18: LIA Oversight
The SWCD and/or GSWCC shall review semi-annually the actions of certified LIA’s
    LIA w/MOA are required to submit additional quarterly reports
The SWCD and/or GSWCC may provide technical assistance to any county or municipality to improve the effectiveness of their erosion and sedimentation control program
The GA EPD may periodically review the actions of certified LIA’s
O.C.G.A. 12-7-8(b)
Notes: Quarterly reports are required per the MOA agreement

## Slide 19: Permitting Process
O.C.G.A. 12-7-9

## Slide 20: LDA Permit
All land disturbing activities, not exempt from GESA, must first secure a Land Disturbing Activity (LDA) Permit from the LIA (if applicable)
It is the responsibility of the property owner/operator to obtain the LDA Permit
*Local requirements can be more stringent
Notes: *For example, a boat ramp on the Chattahoochee River in Fulton County that disturbs 0.25 acres – a stand alone project – is exempt from NPDES permits, but a LDA Permit from the County is required and a buffer variance from EPD is required

## Slide 21: Plan Submittal
An application for a LDA permit shall be accompanied by an Erosion & Sedimentation Control Plan
The Plan shall contain a certification stating that the plan preparer or the designee thereof visited the site prior to the creation of the plan
In any event, permits shall be issued no later than 45 days after the application has been filed with the LIA
O.C.G.A. 12-7-9(a-c)

## Slide 22: Plan Submittal
LIA w/o MOA
LIA w/ MOA
Owner/Operator
  Submits application with Plan
LIA
  Receives application with Plan
  Forwards Plan for review within 10 days
SWCD
  Technical review conducted by GSWCC or NRCS
  Ratifies the Plan
  35 days upon receipt per submittal to approve or deny
Owner/Operator
  Submits application with Plan
LIA
  Receives application with Plan
  Approves or denies the Plan
  45 days upon receipt to issue or deny permit application
O.C.G.A. 12-7-10
Failure to act within timeframe constitutes an automatic approval

## Slide 23: Plan Submittal
No LIA
Owner/Operator
  Submits single copy of the Plan to the GA EPD Watershed Protection Branch
  Submits second copy to the corresponding GA EPD District office
GA EPD
  GA EPD Watershed Protection Branch reviews the Plan for deficiencies and may provide comments
  Enforcement conducted by GA EPD District office
EPD does not issue a LDA Permit

## Slide 24: Plan Submittal
Project not regulated by a Local Issuing Authority
(GA DOT, GA Power, Poultry House, Public Drinking Reservoir)
Owner/Operator
  Submits single copy of the Plan to the GA EPD Watershed Protection Branch
  Submits second copy to the corresponding GA EPD District office
GA EPD
  GA EPD Watershed Protection Branch reviews the Plan for deficiencies and may provide comments
  Enforcement conducted by GA EPD District office
EPD does not issue a LDA Permit

## Slide 25: Enforcement Options
O.C.G.A. 12-7-7
O.C.G.A. 12-7-11
O.C.G.A. 12-7-12
O.C.G.A. 12-7-15

## Slide 26: Possible Actions
Notice of Violation
Issuance of Stop Work Order
Suspension of LDA Permit
Denial of future LDA Permit applications
Imposition of civil penalties
Forfeiture of bonding

## Slide 27: Notice of Violation
First & Second Violation
  A written warning is issued to the permittee
  The permittee shall have five (5) days to correct the violation
  If the violation is not corrected within five (5) days, an immediate stop work shall be issued
Third Violation
  An immediate stop work order shall be issued
O.C.G.A. 12-7-12(c)

## Slide 28: Stop Work Order
Immediate Issuance
  3rd violation
  Imminent threat to public health
  Land disturbance without a permit
  Failure to maintain stream buffer
  Significant amounts of sediment discharged into state waters
  Where BMPs have not been properly designed, installed, and maintained
All Stop Work Orders
  Effective immediately upon issuance
  In effect until corrective action or mitigation has occurred
  Apply to all land-disturbing activity on the site with the exception of the installation and maintenance of all erosion and sediment controls
  Can be issued with a NOV
O.C.G.A. 12-7-12(d)

## Slide 29: Suspension of LDA Permit
The LDA Permit may be suspended, revoked, or modified by the LIA if the permit holder is not in compliance with the approved Erosion & Sediment Control Plan or if there is any violation
O.C.G.A. 12-7-11(b)

## Slide 30: Denial of Future LDA Permits
If a permit applicant has had two (2) or more violations of previous permits within three (3) years prior to the date of filing of the application under consideration, the Local Issuing Authority may deny the permit application.
O.C.G.A. 12-7-7(f)(1)

## Slide 31: Civil Penalties
A maximum penalty of $2500 for each violation shall be imposed by the municipal or magistrate courts
Each day during which the violation or failure or refusal to comply continues shall be a separate violation
O.C.G.A. 12-7-15

## Slide 32: Forfeiture of Bonding
The LIA may require the permit applicant to post a bond in the form of:
    Government security
    Cash
    Irrevocable letter of credit
    Combination thereof
Up to $3000/acre of the proposed land-disturbing activity
If the applicant doesn’t comply with permit, the bond may be forfeited and the proceeds may be used to hire a contractor to stabilize the site and bring it into compliance
O.C.G.A. 12-7-7(f)(2)
Notes: Bonding is not a common enforcement tool, but it is very effective. It should be used more often by Local Issuing Authorites. This option prevents sites from being out of compliance for months to even years

## Slide 33: Exemptions
O.C.G.A. 12-7-17

## Slide 34: Surface Mining
"Surface mining" means any activity constituting all or part of a process for the removal of minerals, ores, and other solid matter for sale or for processing or for consumption in the regular operation of a business. Tunnels, shafts, borrow pits of less than 1.1 disturbed acres, and dimension stone quarries shall not be considered to be surface mining.
O.C.G.A. 12-4-72(15)
O.C.G.A. 12-7-17(1)
Notes: Surface mining is defined in O.C.G.A. 12-4-72(15)

## Slide 35: Granite Quarrying
Granite quarrying and the land clearing for such quarrying
O.C.G.A. 12-7-17(2)

## Slide 36: Minor Land Disturbing Activities
Home gardens
Home landscaping
Repairs
Maintenance
Fences
Other related activities which result in minor soil erosion
O.C.G.A. 12-7-17(3)
N/A for activities that are located within the State-mandated Buffer on sites covered by the State General Permits

## Slide 37: Single-Family Residences
When
  Construction disturbs < one (1) acre
  Not part of a larger common plan of development
ES&PC Plan & Buffer requirements still apply
O.C.G.A. 12-7-17(4)
Exempt from LDA Permit only

## Slide 38: Agricultural Operations
Practices involving the establishment, cultivation, or harvesting of products of the field or orchard
Preparation and planting of pasture land
Farm ponds
Dairy operations
Livestock & Poultry management practices
Construction of farm buildings (Not exempt from NPDES)
O.C.G.A. 12-7-17(5)
O.C.G.A. 1-3-3
Notes: Agriculture is defined in O.C.G.A. 1-3-3
Farm Buildings (i.e. Chicken Houses, etc..) are NOT exempt from NPDES permitting

## Slide 39: Forestry Practices
Forestry land management practices, including harvesting
When such activities result in a buffer encroachment, a 3 year moratorium is placed on the entire property
O.C.G.A. 12-7-17(6)
Forestry Land Management Practices/Silvicultural Practices Exemption Guidelines – March 2010 (epd.georgia.gov)

## Slide 40: NRCS Projects
Projects carried out under the technical supervision of the USDA-NRCS
O.C.G.A. 12-7-17(7)

## Slide 41: Projects < 1.0 Acre
Any project involving less than one (1) acre of disturbed area unless the land-disturbing activity is:
    Within a larger common plan of development with a planned disturbance equal to or greater than 1.0 acre
    Or within 200 ft. of the bank of any perennial stream
If a project, located in a area with no Certified LIA, is less than one (1) acre AND within 200 ft. of a perennial stream, no plan submittal is required but the buffer requirements would still be applicable
O.C.G.A. 12-7-17(8)
Check local requirements

## Slide 42: Road Projects
Any projects undertaken or financed by:
  Department of Transportation
  GA Highway Authority
  State Road & Tollway Authority
Any road construction or maintenance project, or both, undertaken by any county or municipality
Not exempt if located within a larger common plan of development
  Becomes secondary permittee; Enforced by LIA
O.C.G.A. 12-7-17(9)
Not exempt from NPDES

## Slide 43: Utility Projects
Any land-disturbing activities conducted by:
  Electric Membership Corporation
  Municipal Electrical System
  Public Utility under PSC jurisdiction (i.e. Solar Farms & Railroads)
  Any utility under FERC jurisdiction
  Cable television systems
Not exempt if located within a larger common plan of development
  Becomes secondary permittee; Enforced by LIA
O.C.G.A. 12-7-17(9)
Not exempt from NPDES
Notes: PSC – Public Service Commission
FERC – Federal Energy Regulatory Commission

## Slide 44: Utility Projects
Not exempt from NPDES

## Slide 45: Public Water System Reservoirs
O.C.G.A. 12-7-17(11)
Not exempt from NPDES

## Slide 46: Education & Training Requirements
O.C.G.A. 12-7-19

## Slide 47: Who Must Be Certified?
Persons involved in land development design, review, permitting, construction, monitoring, or inspection or any land-disturbing activity shall meet the education and training certification requirements, dependent on his or her level of involvement with the process as developed by the Commission in consultation with the GA EPD and the Stakeholder Advisory Board
O.C.G.A. 12-7-19(a)(1)
Notes: Regulatory authorities have to meet certification requirements as well as enforce certification requirements on site

## Slide 48: Who Must Be Certified On Site?
Whenever land-disturbing activities are being conducted on site, each entity or person acting as either a primary, secondary, or tertiary permittee shall have as a minimum one (1) person who is responsible charge of erosion and sedimentation control activities
Persons or entities involved in projects not requiring a state general permit but otherwise requiring certified personnel on site may contract with certified persons
O.C.G.A. 12-7-19(a)(2-3)

## Slide 49: Courses
Notes: Although not required, it is a good idea for elected officials to become aware of the minimum requirements

## Slide 50: Certification Card Substitution

## Slide 51: Subcontractor Awareness Seminar
Required for individuals involved in land disturbing activities that are working in a subcontractor capacity for a primary, secondary or tertiary permittee
Individuals working in a subcontractor capacity cannot be required to meet any educational requirements that exceed those of a Certified Subcontractor
Certified Subcontractor status DOES NOT certify an individual to perform the duties of a “certified” person/personnel
If an individual is performing “certified” duties, a Level 1A certification is required

## Slide 52: Subcontractor Awareness Seminar
If an individual is working in a subcontractor capacity and possesses a Level 1A certification they are not required to take the Subcontractor Awareness Seminar
If an individual is working in a subcontractor capacity and has attended a Level 1A course, they are not required to take the Subcontractor Awareness Seminar. They can:
    Complete a Subcontractor Awareness Application
    Submit a Proof of Attendance form from the Level 1A course

## Slide 53: Certification Cards
Cards are color coded by level of certification for quick reference in the field
  Level 1A – Blue
  Level 1B – Red
  Level II Plan Reviewer – Gray
  Level II Design Professional – Tan
  Subcontractor Awareness – White
Regulatory inspectors should ask to see certification cards on-site

## Slide 54: Certification Cards
Name
Certification # is the same for all levels
Level 1A Blue Card
All certifications are valid for 3 years

## Slide 55: Re-Certification Requirements
A certification provided by achieving the requirements established by GSWCC shall expire no later than three (3) years after its issuance
A certified individual shall be required to attend and participate in at least four (4) hours of approved continuing education courses, as established by GSWCC, every three (3) years
Individuals may begin taking re-certification courses one (1) year before their initial certification expires
    Courses taken before the 1 year mark will not count as credit
O.C.G.A. 12-7-19(e)(1-2)

## Slide 56: Re-Certification Requirements
An individual who wishes to renew their certification shall attend four (4) hours of continuing education (CE) for each certification they wish to renew
Example
  John Doe is a Certified Inspector & Certified Plan Reviewer
  He must attend 4 hours of CE for Level 1B & 4 hours of CE for Level II
There is no exam for any re-certification course
Re-certification cards are mailed out two (2) weeks before expiration

## Slide 57: Course Listings
For additional information and a complete list of upcoming courses
  http://www.gaswcc.org/esc-courses.php

## Slide 58: Summary
GESA is the State Law that governs land-disturbing activities
All eligible activities must first secure a LDA permit
Counties and municipalities can become a LIA when certified by the GA EPD
One person from each entity shall meet the education and certification requirements dependent on their level of involvement

## Slide 59: Questions?
GSWCC
Urban Program
4310 Lexington Road
Athens, GA 30605
(706) 552-4474