## Slide 1: Common Issues on Site
Level 1A Recertification
Effective August 2018
Structural & Vegetative Measures

## Slide 2: Maintenance
A series of properly designed, installed, and MAINTAINED BMPs shall constitute a complete defense to any regulatory enforcement
A BMP cannot function properly if it is not being properly maintained
Permittees should be inspecting BMPs on a daily, weekly, and monthly basis
All reporting to EPD is to be done electronically in GEOS

## Slide 3: Field Manual
The current 2016 edition of the Field Manual for Erosion & Sediment Control in Georgia contains maintenance requirements for each structural and vegetative BMP
Can be found at:
  www.gaswcc.georgia.gov
Notes: As well as the Green Book & ES&PC Plan

## Slide 4: Example (Sd1)

## Slide 5: What to Look For
  Lime requirements
  Fertilizer requirements
  Mulching
  Re-seeding
  Mowing
  Inspections
  Monitoring
  De-mucking
  Clean-out depths
  Replacing materials
Vegetative Measures
Structural Measures

## Slide 6: Documentation
If any BMP is in need of maintenance, it should be noted in the permittee inspection reports
Include all observations related to each individual BMP
Document on the reports the fix for each maintenance requirement
Document compliant BMPs on all inspection reports as well

## Slide 7: Vegetative Measures
Common Maintenance Requirements

## Slide 8: Ds1 - Mulching
90% cover is not being
maintained

## Slide 9: Ds1 - Mulching
Straw/hay shall be at a depth of 2”-4”
Notes: Proper mulching depth

## Slide 10: Ds2 – Temporary Vegetation
Area in need of temporary
seeding
Notes: Even roads after 14 days of sitting idol need stabilization if left alone.

## Slide 11: Ds2 – Temporary Vegetation
An adequate stand has failed to emerge. Re-seeding may be
needed
Sedimentation can also inhibit plant growth by screening out
sunlight

## Slide 12: Ds2 – Temporary Vegetation
Properly stabilized stand
A top growth of 6” should be maintained at all
times
Notes: Picture shows Brown top millet which is warm season temporary vegetation.

## Slide 13: Structural Measures
Common Maintenance Requirements

## Slide 14: Co – Construction Exit
Co shall be maintained in a condition that will not
allow mud onto the streets
Geotextile underliner?
Mud shall be immediately removed from
roadway
Refresh stone

## Slide 15: Co – Construction Exit
Proper
Construction Exit
Co should be periodically dressed with 1.5”
– 3.5” stone
Notes: 20’x50’ with 1.5-3.5 inch stone

## Slide 16: Dn1 – Temporary Downdrain
The dike ridge over top of the pipe was not properly
compacted
If the maximum drainage area is being exceeded for each structure, a design
change would be needed
Improper installation

## Slide 17: Dn1 – Temporary Downdrain
Properly stabilized
Stakes should always be used to
anchor pipe

## Slide 18: Rt - Retrofit
Rt shall be cleaned out at 1/3rd full
A Rt should have 1” holes that are 8-10”
apart
Notes: Temporary structure that shall be removed at final stabilization

## Slide 19: Rt - Retrofit
Rt shall be affixed to the outlet control structure

## Slide 20: Sk – Floating Surface Skimmer
Skimmer shall be freed from the accumulated sediment to allow
normal operation

## Slide 21: Sk – Floating Surface Skimmer
Skimmer resting on metal bar out of the accumulated
sediment

## Slide 22: St – Storm Drain Outlet Protection
Pond should discharge clean water. This should be cleaned out and
riprap replaced
Notes: This is likely indicative of another maintenance problem on the site such as a failure to maintain the pond and properly stabilize the site

## Slide 23: St – Storm Drain Outlet Protection
An incorrect installation can lead to additional
maintenance needs
Notes: What is wrong with this outlet protection on some of the st’s in the picture? In the closest st the water comes out with such velocity that it misses half of the St causing more erosion in the bottom of the sediment pond

## Slide 24: St – Storm Drain Outlet Protection
Proper Outlet Protection

## Slide 25: Sd1 – Sediment Barrier
Sd1 shall be cleaned out at ½
full
The 1st row is completely full
2nd
Row
The space between the rows should be at least 36”

## Slide 26: Sd1 – Sediment Barrier
Sd1 is to maintain 80% of its properly designed height

## Slide 27: Sd1 – Sediment Barrier
Silt fence is to be trenched in a minimum of 6
inches

## Slide 28: Are These the Right BMPs?
Sd1 is not designed to be placed in
concentrated flow
A sediment storage BMP would be a better choice for
this area

## Slide 29: Sd2 – Curb Inlet Protection
Proper installation

## Slide 30: Sd2 – Curb Inlet Protection
Sediment shall be removed from curb inlet protection
immediately
If inlet cannot drain properly, ponding can occur

## Slide 31: Sd2 – Inlet Protection
Proper Sd2 installation
Sd2-BB
Notes: Sd2-BB (Baffle box)

## Slide 32: Sd2 – Excavated Inlet Protection
Sd2 shall be cleaned out at ½
full
Filter fabric and frame should be
replaced

## Slide 33: Sd2 – Excavated Inlet Protection
Properly excavated Sd2 shown in conjunction with a
Filter Ring

## Slide 34: Sd3 – Temporary Sediment Basin
Sd3 shall be cleaned out at
1/3rd full

## Slide 35: Example Clean-out Marker
Notes: For temporary and permanent ponds

## Slide 36: Sd4 – Temporary Sediment Trap
Sd4 shall be cleaned out at
1/3rd full

## Slide 37: Tp - Topsoil
Stockpile should be stabilized with temporary vegetative
measures
Stockpile should be contained by sediment barriers

## Slide 38: Summary
Remember to use the approved ES&PC Plan & Field Manual for guidance when it comes to maintenance requirements
Failure to maintain BMPs can result in possible enforcement, loss of resources (time, money, etc…), and even civil suits
Using a series of sound BMPs that are properly (1) designed, (2) installed, and (3) maintained is the only way to prevent problems from occurring on site

## Slide 39: Questions?
GSWCC
Urban Program
4310 Lexington Road
Athens, GA 30605
(706) 552-4474